## Slide 1: Applying Models of Auditory Processing to Automatic Speech Recognition: Promise and Progress
Richard Stern
(with Chanwoo Kim, Yu-Hsiang Chiu, and others)
Department of Electrical and Computer Engineering
and Language Technologies Institute
Carnegie Mellon University
Pittsburgh, Pennsylvania 15213
Telephone: +1 412 268-2535; FAX: +1 412 268-3890
Email: rms@cs.cmu.edu; http://www.ece.cmu.edu/~rms
2014 Frederick Jelinek Memorial Workshop on
Meaning Representations in Language and Speech Processing
Prague, Czech Republic
July 16, 2014

## Slide 2: Introduction – auditory processing and automatic speech recognition
I was originally trained in auditory perception, and my original work was in binaural hearing
Over the past 20-25 years, I have been spending the bulk of my time trying to improve the accuracy of automatic speech recognition systems in difficult acoustical environments
In this talk I would like to discuss some of the ways in my group (and many others) have been attempting to apply knowledge of auditory perception to improve ASR accuracy
  Comment: approaches can be more or less faithful to physiology and psychophysics

## Slide 3: The big questions ….
How can knowledge of auditory physiology and perception improve speech recognition accuracy?
Can speech recognition results tell us anything we don’t already know about auditory processing?
What aspects of the processing are most valuable for robust feature extraction?
Notes: Re comment ….. Ignorant, and boundaries fuzzy w CASA and others

## Slide 4: Two historical notes
Everything is changing with deep learning
  Is there a role for “traditional” robust speech technologies?
Knowledge-based versus statistically-based processing

## Slide 5: So what I will do is ….
Briefly review some of the major physiological and psychophysical results that motivate the models
Briefly review and discuss the major “classical” auditory models of the 1980s
  Seneff, Lyon, and Ghitza
Review some of the major new trends in today’s models
Talk about some representative issues that have driven work as of late at CMU and what we have learned from them

## Slide 6: Speech recognition as pattern classification
Major functional components:
  Signal processing to extract features from speech waveforms
  Comparison of features to pre-stored representations
Important design choices:
  Choice of features
  Specific method of comparing features to stored representations
Feature extraction
Decision making
procedure
Speech features
Utterance
hypotheses

## Slide 7: Default signal processing: Mel frequency cepstral coefficients (MFCCs)
Comment: 20-ms time slices are modeled by smoothed spectra,
with attention paid to auditory frequency selectivity

## Slide 8: What the speech recognizer sees ….
An original spectrogram: Spectrum “recovered” from MFCC:

## Slide 9: Comments on the MFCC representation
It’s very “blurry” compared to a wideband spectrogram!
Aspects of auditory processing represented:
  Frequency selectivity and spectral bandwidth (but using a constant analysis window duration!)
    Wavelet schemes exploit time-frequency resolution better
  Nonlinear amplitude response
Aspects of auditory processing NOT represented:
  Detailed timing structure
  Lateral suppression
  Enhancement of temporal contrast
  Other auditory nonlinearities

## Slide 10: Basic auditory anatomy
Structures involved in auditory processing:

## Slide 11: Excitation along the basilar membrane (courtesy James Hudspeth, HHMI)
Notes: FIND SOURCE AND CREDIT!!

## Slide 12: Central auditory pathways
There is a lot going on!
For the most part, we only consider the response of the auditory nerve
  It is in series with everything else

## Slide 13: Transient response of auditory-nerve fibers
Histograms of response to tone bursts (Kiang et al., 1965):
Comment: Onsets and offsets produce overshoot

## Slide 14: Frequency response of auditory-nerve fibers: tuning curves
Threshold level for auditory-nerve response to tones:
Note dependence of bandwidth on center frequency and asymmetry of response

## Slide 15: Typical response of auditory-nerve fibers as a function of stimulus level
Typical response of auditory-nerve fibers to tones as a function of intensity:
Comment:
  Saturation and limited dynamic range

## Slide 16: Synchronized auditory-nerve response to low-frequency tones
Comment: response remains synchronized over a wide range of intensities

## Slide 17: Comments on synchronized auditory response
Nerve fibers synchronize to fine structure at “low” frequencies, signal envelopes at high frequencies
Synchrony clearly important for auditory localization
Synchrony could be important for monaural processing of complex signals as well

## Slide 18: Lateral suppression in auditory processing
Auditory-nerve response to pairs of tones:
Comment: Lateral suppression enhances local contrast in frequency

## Slide 19: Auditory frequency selectivity: critical bands
Measurements of psychophysical filter bandwidth by various methods:
Comments:
  Bandwidth increases with center frequency
  Solid curve is “Equivalent Rectangular Bandwidth” (ERB)

## Slide 20: Three perceptual auditory frequency scales
Bark scale:
(DE)
Mel scale:
(USA)
ERB scale:
(UK)

## Slide 21: Comparison of normalized perceptual frequency scales
Bark scale (in blue), Mel scale (in red), and ERB scale (in green):

## Slide 22: Perceptual masking of adjacent spectro-temporal components
Spectral masking:
  Intense signals at a given frequency mask adjacent frequencies (asymmetrically)
Temporal masking:
  Intense signals at a given frequency can mask successive input at that frequency (and to some extent before the masker occurs!)
These phenomena are an important part of the auditory models used in perceptual audio coding (such as in creating MP3 files)

## Slide 23: The loudness of sounds
Equal loudness contours (Fletcher-Munson curves):

## Slide 24: Summary of basic auditory physiology and perception
Major monaural physiological attributes:
  Frequency analysis in parallel channels
  Preservation of temporal fine structure
  Limited dynamic range in individual channels
  Enhancement of temporal contrast (at onsets and offsets)
  Enhancement of spectral contrast (at adjacent frequencies)
Most major physiological attributes have psychophysical correlates
Most physiological and psychophysical effects are not preserved in conventional representations for speech recognition

## Slide 25: Auditory models in the 1980s: the Seneff model
Overall model:
Detail of Stage II:
  An early well-known auditory model
  In addition to mean rate, used “Generalized Synchrony Detector” to extract synchrony

## Slide 26: Auditory models in the 1980s: Ghitza’s EIH model
  Estimated timing information from ensembles of zero crossings with different thresholds

## Slide 27: Auditory models in the 1980s: Lyon’s auditory model
Single stage of the Lyon auditory model:
  Lyon model included nonlinear compression, lateral suppression, temporal effects
  Also added correlograms (autocorrelation and crosscorrelation of model outputs)

## Slide 28: And one more … Cohen’s model (1989)
  Loudness normalization and transient enhancement novel for the time
  Used successfully as part of many IBM systems

## Slide 29: Perceptual Linear Prediction (Hermansky): pragmatic application of auditory principles
The PLP algorithm is a pragmatic approach to model the auditory periphery
Includes:
  Resampling for frequency warping
  Limited frequency resolution
  Pre-emphasis according to threshold of hearing
  Amplitude compression
  Smoothing using linear prediction
Computational complexity similar to LPCC, MFCC
Sometimes provides better recognition accuracy

## Slide 30: The other standard approach: Perceptual Linear Prediction (PLP, Hermansky ‘90)
Comments:
  A pragmatic approach to auditory modeling
  Pre-emphasis, loudness normalization based on threshold of hearing
  RASTA enhancement provides cepstral normalization and modulation filtering
  Widely used with success today

## Slide 31: Auditory modeling was expensive: Computational complexity of Seneff model
Number of multiplications per ms of speech (from Ohshima and Stern, 1994):

## Slide 32: Summary: early auditory models
The models developed in the 1980s included:
  “Realistic” auditory filtering
  “Realistic” auditory nonlnearity
  Synchrony extraction
  Lateral suppression
  Higher order processing through auto-correlation and cross-correlation
Every system developer had his or her own idea of what was important

## Slide 33: Evaluation of early auditory models (Ohshima and Stern, 1994)
Not much quantitative evaluation actually performed
General trends of results:
  Physiological processing did not help much (if at all) for clean speech
  More substantial improvements observed for degraded input
  Benefits generally do not exceed what could be achieved with more prosaic approaches (e.g. CDCN/VTS in our case).

## Slide 34: Other reasons why work on auditory models subsided in the late 1980s …
Failure to obtain a good statistical match between characteristics of features and speech recognition system
  Ameliorated by subsequent development of continuous HMMs
More pressing need to solve other basic speech recognition problems

## Slide 35: Renaissance in the 1990s!
By the late 1990s, physiologically-motivated and perceptually-motivated approaches to signal processing began to flourish
Some major new trends ….
Computation no longer such a limiting factor
Serious attention to temporal evolution
Attention to reverberation
Binaural processing
More effective and mature approaches to information fusion

## Slide 36: Peripheral auditory modeling at CMU 2004–now
Foci of activities:
  Representing synchrony
  The shape of the rate-intensity function
  Revisiting analysis duration
  Revisiting frequency resolution
  Onset enhancement
  Modulation filtering
  Binaural and “polyaural” techniques
  Auditory scene analysis: common frequency modulation

## Slide 37: Speech representation using mean rate
Representation of vowels by Young and Sachs using mean rate:
Mean rate representation does not preserve spectral information

## Slide 38: Speech representation using average localized synchrony rate
Representation of vowels by Young and Sachs using ALSR:

## Slide 39: The importance of timing information
Re-analysis of Young-Sachs data by Secker-Walker and Searle:
Temporal processing captures dominant formants in a spectral region

## Slide 40: Physiologically-motivated signal processing: the Zhang-Carney model of the periphery
We used the “synapse output” as the basis for further processing

## Slide 41: Physiologically-motivated signal processing: synchrony and mean-rate detection (Kim/Chiu ‘06)
Synchrony response is smeared across frequency to remove pitch effects
Higher frequencies represented by mean rate of firing
Synchrony and mean rate combined additively
Much more processing than MFCCs

## Slide 42: Comparing auditory processing with cepstral analysis: clean speech
Original
spectrogram
MFCC
reconstruction
Auditory
analysis

## Slide 43: Comparing auditory processing with cepstral analysis: 20-dB SNR

## Slide 44: Comparing auditory processing with cepstral analysis: 10-dB SNR

## Slide 45: Comparing auditory processing with cepstral analysis: 0-dB SNR

## Slide 46: Auditory processing is more effective than MFCCs at low SNRs, especially in white noise
Curves are shifted by 10-15 dB (greater improvement than obtained with VTS or CDCN)
[Results from Kim et al., Interspeech 2006]
Accuracy in background noise: Accuracy in background music:

## Slide 47: Do auditory models really need to be so complex?
Model of Zhang et al. 2001: A much simpler model:

## Slide 48: Comparing simple and complex auditory models
Comparing MFCC processing, a trivial (filter–rectify–compress) auditory model, and the full Carney-Zhang model (Chiu 2006):

## Slide 49: The nonlinearity seems to be the most important attribute of the Seneff model (Chiu ‘08)

## Slide 50: Why the nonlinearity seems to help …

## Slide 51: Impact of auditory nonlinearity (Chiu)
MFCC
Learned nonlinearity
Baseline nonlinearity

## Slide 52: PNCC processing (Kim and Stern, 2010,2014)
A pragmatic implementation of a number of the principles described:
  Gammatone filterbanks
  Nonlinearity shaped to follow auditory processing
  “Medium-time” environmental compensation using nonlinearity cepstral highpass filtering in each channel
  Enhancement of envelope onsets
  Computationally efficient implementation

## Slide 53: An integrated front end: power-normalized cepstral coefficients (PNCC, Kim ‘10)

## Slide 54: An integrated front end: power-normalized cepstral coefficients (PNCC, Kim ‘10)

## Slide 55: An integrated front end: power-normalized cepstral coefficients (PNCC, Kim ‘10)

## Slide 56: The nonlinearity in PNCC processing (Kim)

## Slide 57: Frequency resolution
Examined several types of frequency resolution
  MFCC triangular filters
  Gammatone filter shapes
  Truncated Gammatone filter shapes
Most results do not depend greatly on filter shape
Some sort of frequency integration is helpful when frequency-based selection algorithms are used

## Slide 58: Analysis window duration (Kim)
Typical analysis window duration for speech recognition is ~25-35 ms
Optimal analysis window duration for estimation of environmental parameters is ~75-120 ms
Best systems measure environmental parameters (including voice activity detection over a longer time interval but apply results to a short-duration analysis frame

## Slide 59: Temporal Speech Properties: modulation filtering
Output of speech and noise segments from 14th Mel filter (1050 Hz)
Speech segment exhibits
greater fluctuations

## Slide 60: Nonlinear noise processing
Use nonlinear cepstral highpass filtering to pass speech but not noise
Why nonlinear?
  Need to keep results positive because we are dealing with manipulations of signal power

## Slide 61: Asymmetric lowpass filtering (Kim, 2010)
Overview of processing:
  Assume that noise components vary slowly compared to speech components
  Obtain a running estimate of noise level in each channel using nonlinear processing
  Subtract estimated noise level from speech
An example:
Note: Asymmetric highpass filtering is obtained by subtracting the lowpass filter output from the input

## Slide 62: Implementing asymmetric lowpass filtering
Basic equation: Dependence on
parameter values:

## Slide 63: Block diagram of noise processing using asymmetric filters
Speech-nonspeech partitions are obtained based on a simple threshold test
Asymmetric highpass filtering is always applied; asymmetric lowpass filtering is applied only to non-speech segments

## Slide 64: Computational complexity of front ends
Chart: 
| MFCC | PLP | PNCC | Truncated PNCC
Mults & Divs per Frame | 10742 | 12448 | 21292 | 12809

## Slide 65: Performance of PNCC in white noise (RM)

## Slide 66: Performance of PNCC in white noise (WSJ)

## Slide 67: Performance of PNCC in background music

## Slide 68: Performance of PNCC in reverberation

## Slide 69: Contributions of PNCC components: white noise (WSJ)
+ Temporal masking
+ Noise protection
+ Medium-time time/freq anal
Baseline MFCC with CMN
+ Temporal masking
+ Noise suppression
+ Medium-duration processing
Baseline MFCC + CMN

## Slide 70: Contributions of PNCC components: background music (WSJ)
+ Temporal masking
+ Noise protection
+ Medium-time time/freq anal
Baseline MFCC with CMN
+ Temporal masking
+ Noise suppression
+ Medium-duration processing
Baseline MFCC + CMN

## Slide 71: Contributions of PNCC components: reverberation (WSJ)
+ Temporal masking
+ Noise protection
+ Medium-time time/freq anal
Baseline MFCC with CMN
+ Temporal masking
+ Noise suppression
+ Medium-duration processing
Baseline MFCC + CMN

## Slide 72: Effects of onset enhancement/temporal masking (SSF processing, Kim ‘10)

## Slide 73: PNCC and SSF @Google

## Slide 74: Summary … so what matters?
Knowledge of the auditory system can certainly improve ASR accuracy:
  Use of synchrony
  Consideration of rate-intensity function
  Onset enhancement
  Nonlinear modulation filtering
  Selective reconstruction
  Consideration of processes mediating auditory scene analysis

## Slide 75: Summary: PNCC processing
PNCC processing includes
  More effective nonlinearity
  Parameter estimation for noise compensation and analysis based on longer analysis time and frequency spread
  Efficient noise compensation based on modulation filtering
  Onset enhancement
  Computationally-efficient implementation
Not considered yet …
  Synchrony representation
  Lateral suppression